## Slide 1: ClickMeeting Deep Packet Inspection
Gufran Yesilyurt
Notes: Hi everyone! I hope you are well. I am Gufran Yeşilyurt. Today I am going to present my Deep Packet Inspection about ClickMeeting. But first, it is good to know what is ClickMeeting?

## Slide 2
What is ClickMeeting?
Technologies
Setup
Live Meeting
Live Webinar
On-demand
Results
Notes: ClickMeeting is basically a platform that makes easier to host different type of webinars.

## Slide 3: "Вебінарна кімната ClickMeeting має багато функцій, які добре використовуються та покращують привабливість занять. Грамотно розроблений онлайн-урок із застосуванням гарних інструментів дозволяє передати знання по-новому, надаючи учням нові стимули, завдяки чому вони більш відкриті до набутих знань." (Перцев, 2018)
"The ClickMeeting webinar room has many functions that are well used and
improve the attractiveness of the classes. A well-designed online lesson with the use of good
tools allows one to transfer knowledge in a new way, providing students with new incentives,
thanks to which they are more open to the acquired knowledge" (Pertsev, 2018)
Technologies
Setup
Live Meeting
Live Webinar
On-demand
Results
Notes: There was only research about ClickMeeting’s impact on education in Ukrainian. It was commonly used in Poland and other European countries due to the Covid crisis.

## Slide 4: Key Concepts
Technologies & Protocols
Experimental Setup
Inspection of Packets
1
2
3
Technologies
On-demand Webinar
Experimental Setup
Results
Live Webinar
Live Meeting
Technologies
Setup
Live Meeting
Live Webinar
On-demand
Results
Notes: Today we are going to start with inspecting technologies that are used by ClickMeeting, and hopefully, we are going to understand them. Then I am going to explain how I captured the packets and the things that I pay attention to while I am capturing. After the experimental setup, we are going to analyze different types of webinars and at the end, we will see the results of these analyzes.

## Slide 5
HTML5 - webRTC
Technologies
01.
Technologies
Setup
Live Meeting
Live Webinar
On-demand
Results
Notes: So, let’s start with the technologies.

## Slide 6: Technologies
HTML5 is a markup language used for structuring and presenting content on the World Wide Web.
webRTC is a technology that enables Web sites to capture and optionally stream audio and/or video media.
HTML5
webRTC
Technologies
Setup
Live Meeting
Live Webinar
On-demand
Results
Notes: ClickMeeting uses HTML5 and webRTC. As most of you know these technologies make it much easier to stream videos and audio on browsers due to the codecs they support. In fact that you can use ClickMeeting from browser hence these technologies create an advantage while hosting webinars. But let’s take a closer look at these technologies.

## Slide 7: Historia
The ClickMeeting supports most of the Video and Audio codecs by HTML5.
Codecs
Provides an opportunity to video/audio stream on mobile devices, desktops, and websites.
Responsive
HTML5
Technologies
Setup
Live Meeting
Live Webinar
On-demand
Results
Notes: Here you can see the codecs supported by HTML5. Thanks to these codecs today we are able to encode and decode our data on browsers. As an example, an MP3 codec is used to create MP3 files from audio data. To play that MP3 file back on a computer or separate device, you'll need a codec that can decode the format.

## Slide 8: Historia
WebRTC architecture consists of over a dozen different standards, covering both the application and browser.
Architecture
Unlike all other browser communication that use Transmission Control Protocol (TCP), WebRTC transports its data over User Datagram Protocol (UDP).
Protocols
webRTC
Technologies
Setup
Live Meeting
Live Webinar
On-demand
Results
Notes: webRTC looks actually more complicated. You can see the APIs and Protocols that are used by webRTC. I guess most of you are familiar with UDP and TCP so let’s examine why these are having importance in this presentation.

## Slide 9: Browser vs Desktop
Browser: UDP, STUN, DTLS, SDP
Desktop: TCP, STUN, TLS
Technologies
Setup
Live Meeting
Live Webinar
On-demand
Results
Notes: Because webRTC and HTML5 are used by the browser side, there are some differences with the desktop application. While capturing packets, I noticed that the desktop application transports data over TCP so to understand this difference I chose to inspect it instead of the browser. But of course, there were some other reasons when I made this decision.

## Slide 10
Desktop traffic is easy to isolate rather than browser traffic.
Still, some parts are connected to the website.
Easy
Connected
Notes: Desktop traffic was way easier to isolate and there were still some parts connected to the browser so it was not different from all aspects.

## Slide 11
Wireshark – TCPView – netstat
Experimental Setup
02.
Technologies
Setup
Live Meeting
Live Webinar
On-demand
Results
Notes: Now let’s take a look at how I started to capture and inspect these packets. Of course, it was with Wireshark but there are other tools that are worth mentioning.

## Slide 12: Tools
Find which ports are used by the application (TCPView).
As an alternate to TCPView, find ports by netstat command.
a.
b.
Filter the port in Wireshark and capture packets.
c.
Technologies
Setup
Live Meeting
Live Webinar
On-demand
Results
Notes: Before starting, I can say that as an alternate solution I could use a virtual machine but I had some issues with my virtual machine so I chose this method. In order to isolate network traffic, I had to filter it. So I thought I need to know which port this application uses. If you want to find that you can use TCPView developed by Microsoft or if you like to have dirt in your hands and want to use terminal you can use netstat command to observe port used by proccesses. After that you can easily filter the network traffic by port in Wireshark.

## Slide 13: Pcap Files
Chat, Voice, and Video call with attendees at the same time.
Live Meeting
Chat with attendees but only the presenter’s voice and video stream.
Live Webinar
Pre-recorded stream broadcasts.
On-Demand
Technologies
Setup
Live Meeting
Live Webinar
On-demand
Results
Notes: ClickMeeting doesn’t let you write messages or just voice chat, you must attend a webinar or a meeting so it was not quite easy to detect transitions between chat, voice, and video. That’s why I decided to inspect the differences between different webinar and meetings types. As you can see in the slide, there are different features provided by different types of meetings.

## Slide 14
Technologies
Setup
Live Meeting
Live Webinar
On-demand
Results
Packet Behavior & Features
Live Meeting
03.
Notes: Let’s start with the Live Meeting. This is the meeting type that we are currently doing.

## Slide 15: Packet Lengths
Technologies
Setup
Live Meeting
Live Webinar
On-demand
Results
Notes: As most of you would expect, the lengths of most packets are smaller. This is mostly because of the concerns about packet loss and transportation speed. That’s why in live meetings packets must be smaller.

## Slide 16: Protocol Hierarchy
Technologies
Setup
Live Meeting
Live Webinar
On-demand
Results
Notes: As I have mentioned before, the desktop application sends most of the data over TCP. Also, you may notice that most of the UDP packets are from STUN. The STUN server allows clients to find out their public address, this information is used to set up UDP communication between the client and the VoIP provider to establish a call.

## Slide 17: I/O Graph
Technologies
Setup
Live Meeting
Live Webinar
On-demand
Results
TCP errors (red bars) are not common so these are normal events. They do not impact application and/or performance across the network.
Notes: When we look at the I/O Graphs we can see the packets over time. These arrows indicate the times that I open my mic and video. It is also possible to colorize packets by their protocol but in this case, it is mostly TCP. Also, we can check the packet losses indicated by red bars but there are not many due to the good connection performance.

## Slide 18: TCP Trace
Technologies
Setup
Live Meeting
Live Webinar
On-demand
Results
Green Line: 10.200.30.142 Calculated Receive Window
Brown Line: Acknowledged Data
Notes: AT TCP Trace Graphs we can inspect transmitted data. You may wonder what is the calculated receive window. Simply put, it is a TCP receive buffer for incoming data that has not been processed yet by the application. This field tells how much data can be sent on the wire before an acknowledgment is received. If the receiver is not able to process the data as fast as it arrives, gradually the receive buffer will fill and the TCP window will be reduced in the acknowledgment packets.

## Slide 19: Flow Graph
Technologies
Setup
Live Meeting
Live Webinar
On-demand
Results
The Flow Graph window shows connections between hosts. It displays the packet time, direction, ports, and comments for each captured connection.
Notes: As it stated in the slide, flow graph makes it easier to see communication between sources and destinations. With this way you can also see if is there any Proxy servers.

## Slide 20
Technologies
Setup
Live Meeting
Live Webinar
On-demand
Results
Packet Behavior & Features
Live Webinar
04.
Notes: Now let’s continue with the live webinars. I mostly introduced and described the features of graphs before so in this part we will be more familiar about what they are telling us.

## Slide 21: Packet Lengths
Technologies
Setup
Live Meeting
Live Webinar
On-demand
Results
Notes: Not surprisingly, packets are similar to the Live Meeting. Why? Because they are not so different actually. Live webinars are just like live meetings but attendants can’t open their video or mic. Most of the other features are the same.

## Slide 22: Protocol Hierarchy
Technologies
Setup
Live Meeting
Live Webinar
On-demand
Results
Notes: There is one difference between Live meetings. There are not any packets by QUIC. I am not quite sure but I guess that the application may disable QUIC in Live Webinars due to security concerns.

## Slide 23: Flow Graph
Technologies
Setup
Live Meeting
Live Webinar
On-demand
Results
Thanks to the Flow Graph, it can be clearly observed which IP addresses are connected.
Notes: We can see that connection established mostly between same IP addresses.

## Slide 24
Packet Behavior & Features
On-Demand Meeting
05.
Technologies
Setup
Live Meeting
Live Webinar
On-demand
Results
Notes: In this part, there will be differences. You can guess the reason behind this. Because it is not live. Attendants are just watching a video actually. I shared a 2K resouliton video but I guess platform streams it with HD quality.

## Slide 25: Packet Lengths
Technologies
Setup
Live Meeting
Live Webinar
On-demand
Results
Notes: Packet lengths are radically increased. Even though I researched I couldn’t find any reasonable explanation for that because I would expect to send smaller packets with UDP while streaming video.

## Slide 26: Protocol Hierarchy
Technologies
Setup
Live Meeting
Live Webinar
On-demand
Results
Notes: All packets are transported over TCP. This may be because attendants just had to download the video and didn’t need to find the public address of the servers so didn’t use any STUN protocol.

## Slide 27: I/O Graph
Technologies
Setup
Live Meeting
Live Webinar
On-demand
Results
I/O Graphs let us plot packet and protocol data in a variety of ways.
Notes: It looks clearer than live streams because packets are sent according to the buffer so there are spikes.

## Slide 28: Flow Graph
Technologies
Setup
Live Meeting
Live Webinar
On-demand
Results
No communication with any IP address except local network and clickmeeting’s amazon servers as video is played from a single connection.
Notes: This may be because I was the only attendant. But we can see a clear communication between just local network and the server.

## Slide 29: Comparison
While there are data where UDP is used during live streaming, only TCP is used during the on-demand webinar.
While live-streaming voice and video calls, smaller packets are transported, but in video recording, the packets are much larger.
Protocol Hierarchy
Packet Sizes
Technologies
Setup
Live Meeting
Live Webinar
Results
On-demand
Notes: As a result, let’s compare protocols and packet sizes. We can clearly see the differences between on-demand connections and live streams while there are similarities between live meetings and live webinars. Also, packet sizes were bigger for on-demand video sharing even though I don’t know the logical reason behind it.

## Slide 30: Servers - Subdomains
Nmapper
DNS Dumpster
Technologies
Setup
Live Meeting
Live Webinar
Results
On-demand
(Not Real Locations)
Notes: At last, I scanned the IP addresses to find domain names. I have found some of the servers but more importantly this scan led to a vulnerability which is about subdomains. ClickMeeting creates subdomains for every user-created starting with their username. This may cause leaks about users’ personal information or phishing attacks.

## Slide 31: To Sum Up
Tech | Setup | Live Meeting | Live Webinar | On-Demand | Results
HTML5 - webRTC | Wireshark - Ports | Chat – Voice - Video | Chat – Voice - Video (Just Host) | Recorded Video | Comparison
Technologies
Setup
Live Meeting
Live Webinar
Results
On-demand
Notes: To sum up we can remember that HTML5 and webRTC have great importance on browsers. Then we set up our Wireshark with the guidance of our port scan. Then we inspected the features and network traffics of live and on-demand streams. In the end, we compared similarities and differences between packets and found a possible vulnerability at ClickMeeting.

## Slide 32: Thanks!
Presented by Gufran Yesilyurt
Technologies
Setup
Live Meeting
Live Webinar
Results
On-demand
Notes: Many thanks for your time and patience!

## Slide 33: References
Pertsev M. (2018), SYNCHRONOUS LEARNING IN ONLINE COURSE: A NECESSITY OR CHOICE?
About ClickMeeting. (2022, March 18). Help Center Clickmeeting. https://knowledge.clickmeeting.com/faq/what-technology-does-clickmeeting-use/
HTML5 media. (n.d.). O’Reilly Online Learning. https://www.oreilly.com/library/view/html5-media/9781449308063/ch01.html
WebRTC. (2013, October 15). High Performance Browser Networking. https://hpbn.co/webrtc/
WebRTC – architecture & protocols. (2017, August 19). P's Blog. https://princiya777.wordpress.com/2017/08/19/webrtc-architecture-protocols/
Markruss. (2022, January 27). TCPView for Windows - Windows Sysinternals. Developer tools, technical documentation and coding examples | Microsoft Docs. https://docs.microsoft.com/en-us/sysinternals/downloads/tcpview
Technologies
Setup
Live Meeting
Live Webinar
Results
On-demand
Notes: Here are the references that helped me while doing this inspection.